## Slide 1
Plant Disease Detection Using Hyperspectral Imaging
Explainable Edge-AI for Grapevine and Tomato Disease Diagnosis with Multilingual Advisory
Deep learning | Grad-CAM | Hyperspectral band analysis | Raspberry Pi 5

## Slide 2
Project Overview
PlantDiseaseAI
2
An intelligent plant-health analysis system that identifies plant diseases and examines subtle changes in leaf condition.
Predicts
Possible plant disease
Confidence score
Grapevine and tomato crops
Explains
Grad-CAM highlights affected leaf regions
Wavelength-specific band analysis
Spectral profile per ROI
Advises
Prevention, remedies and tips
English, Hindi and Marathi
Excel result export

## Slide 3
Problem and Motivation
PlantDiseaseAI
3
Why diagnosis is hard
Early symptoms of different diseases look alike
Expert agronomists are scarce
RGB cameras average away narrow spectral changes
Limits of black-box CNNs
A label without justification
May be right for the wrong reason
Often needs cloud or GPU
Our answer
Show where on the leaf and in which wavelengths the evidence lies
Run offline on low-cost hardware
Speak the grower’s language

## Slide 4
Objectives
PlantDiseaseAI
4
1
Classify grapevine (4 classes) and tomato (10 classes) leaf diseases
2
Explain each decision with Grad-CAM heatmaps
3
Reconstruct a 401-band spectrum (380–780 nm) from RGB
4
Provide a GUI with ROI selection, spectral graph and gain control
5
Deliver prevention, remedies and tips in three languages
6
Export results to Excel and run on a Raspberry Pi 5

## Slide 5
System Architecture
PlantDiseaseAI
5
Input
Pi Camera / image file
›
Preprocess
Resize, normalise
›
Prediction
EfficientNet-B0
›
Explain
Grad-CAM overlay
›
Spectral
RGB → 401 bands
›
Output
Advice, Excel
Desktop and edge GUI
PyQt6 with dual image viewports
Rubber-band ROI, live spectral graph
Edge hardware
Raspberry Pi 5, Camera Module 3
5000 K LED ring chamber, 7-inch touch panel

## Slide 6
Dataset and Preprocessing
PlantDiseaseAI
6
4,062
Grapevine images, 4 classes
18,160
Tomato images, 10 classes
70:15:15
Train / val / test, seed 42
≤ 5
pHash Hamming distance
Source and splits
PlantVillage colour subset
Grape: 2,843 / 609 / 610
Tomato: 12,712 / 2,724 / 2,724
Stratified random sampling
Pipeline
Resize: 224×224 grape, 256×256 tomato
ImageNet normalisation
Flip, rotation, shear, scale, colour jitter
Class-weighted loss for imbalance

## Slide 7
Deep Learning Model and Training
PlantDiseaseAI
7
EfficientNet-B0
Pretrained transfer learning, about 4.0 M parameters
MBConv blocks with squeeze-and-excitation, SiLU
Heads: 4 outputs (grape), 10 outputs (tomato)
Runs on CPU, GPU and Raspberry Pi 5
Training setup
AdamW, weight decay 1e-4
Cosine annealing: 1e-3 down to 1e-5
Batch 32, up to 50 epochs, mixed precision
Gradient clipping at 1.0
Early stopping: grape at epoch 15, tomato at epoch 38
Validation accuracy 100% at stop

## Slide 8
Explainable AI: Grad-CAM
PlantDiseaseAI
8
How it works
Hooks on features[-1][0], the final 1280-channel layer
Gradient-weighted channel importance, then ReLU
Jet colormap blended at α = 0.45
Human in the loop
Lesion-focused map: accept the result
Background-focused (fingers, glare, bench): re-image
Spectrum gives an independent cross-check
The overlay shows the network’s attention on a leaf, so a user can reject a result that looks right for the wrong reason.

## Slide 9
Hyperspectral Reconstruction from RGB
PlantDiseaseAI
9
SpectrumTransfer
Colour features [R, G, B, R², G², B²]
6 PCA components, 401 bands, 380–780 nm
Calibrated with CIE colour matching and D65
Reflectance | Healthy | Infected
550 nm (green peak) | 24.8% | lowered
670 nm (chlorophyll dip) | 8.2% | 27.4%
750 nm (NIR shoulder) | 53.4% | 24.1%
Infected tissue: red reflectance rises and the near-infrared plateau collapses. The spectrum is a statistical estimate from RGB, not a measurement.

## Slide 10
Narrow Band Analysis Feature
PlantDiseaseAI
10
Wavelength-specific analysis: examines individual narrow spectral bands to observe variations at specific wavelengths.
Detection of subtle changes: visualises minor variations that are hard to distinguish in normal images.
Spectral data analysis: extracts wavelength-specific information to compare leaf regions.
Plant health assessment: adds visual and spectral information to support investigation of disease-related changes.
Enhanced interpretation: complements deep-learning prediction and Grad-CAM with another perspective.
Bands in the app
Band 1: 400–450 nm
Band 2: 500–550 nm
Band 3: 600–650 nm
Band 4: 700–750 nm
All bands: 400–750 nm
Gain control 1.0x to 8.0x
Key benefit: a more detailed view of leaf characteristics by examining wavelength-specific information beyond the three colour channels of a standard RGB image.

## Slide 11
Results and Benchmarks
PlantDiseaseAI
11
99.18%
Grape accuracy, N = 610
98.42%
Tomato accuracy, N = 2,724
99.13%
Grape macro-F1
98.28%
Tomato macro-F1
Platform (batch 1) | Inference + Grad-CAM | FPS | Peak memory
Desktop CUDA GPU | 11.4 + 4.2 = 15.6 ms | 64.1 | 1.12 GB VRAM
Desktop CPU (Intel i7) | 42.6 + 15.8 = 58.4 ms | 17.1 | 435 MB RAM
Raspberry Pi 5 | 124.8 + 36.5 = 161.3 ms | 6.2 | 365 MB RAM

## Slide 12
Application: Disease Prediction with Grad-CAM
PlantDiseaseAI
12
On screen
Original image and Grad-CAM overlay
ROI box with spectral profile
Disease name and confidence
Prevention, remedies, tips
Gain control and Excel export

## Slide 13
Multilingual Support: Hindi Interface
PlantDiseaseAI
13
Language switch
English, Hindi, Marathi
Disease names and remedies in the chosen language
Narrow-band view (Band 2, 500–550 nm) beside the original

## Slide 14
Prototype and Field Demonstration
PlantDiseaseAI
14
Prototype on a 7-inch touch display, shown during a live demonstration.

## Slide 15
Advisory and Excel Export
PlantDiseaseAI
15
Trilingual advisory
ICAR and MPKV terminology
Organic: Bordeaux mixture 1%, Trichoderma viride, NSKE 5%
Chemical: Mancozeb, Difenoconazole, Copper Oxychloride, Metalaxyl
Prevention and management tips
Excel workbook (3 sheets)
Spectral Intensity Data: wavelength 380–780 nm per ROI
Analysis Summary: disease, confidence, ROI area, reflectance, date
Graph: embedded spectral curve image

## Slide 16
Conclusion and Future Scope
PlantDiseaseAI
16
Conclusion
Accurate: 99.18% grape, 98.42% tomato
Explainable: Grad-CAM plus spectral view
Offline: 6.2 FPS on Raspberry Pi 5
Accessible: three languages, Excel records
Future scope
UAV multispectral imaging
INT8 quantisation and NPU acceleration
Mobile field deployment
Field-image training and spectrometer validation